## Slide 1
Covariance Map Matching (CMM)
Probabilistic Propagation with GNSS Uncertainty and
Trustworthiness Evaluation for Mismatch Prevention
Reporter: Chenzhang Ning
2026

## Slide 2
Presentation Outline
1
Problem & Motivation
GNSS uncertainty challenge; why covariance matters; core contributions
2
Probabilistic Propagation
Emission probability; Jacobian reprojection; PHMI integrity framework
3
Transition Model & Viterbi
UBODT-based transition; log-space Viterbi; gap bridging
4
Trustworthiness Evaluation
Layer entropy & ΔH; sliding-window margin; diagnostic fault classification
5
Results & Conclusion
System architecture; config parameters; future directions

## Slide 3
Section 1: Problem & Motivation

## Slide 4
1 — The Map Matching Challenge Under Uncertainty
Classic HMM Map Matching
Assumes isotropic, fixed-variance GPS error
Emission probability: P ∝ exp(−dist² / 2σ²) — circular
Single σ parameter per dataset
Works for open-sky, static environments
Real GNSS Reality
Anisotropic error: urban canyons, multipath, satellite geometry
Per-epoch covariance from receiver (6 elements):
sde, sdn — East/North standard deviation
sdne — North-East covariance (off-diagonal term)
Protection levels bound maximum position error
Maps also have digitization error (centerline offset)
CMM uses the full 2D covariance matrix + protection levels, not just a scalar distance. This is the key differentiator from classic Hidden Markov Map Matching.
// cmm_algorithm.hpp:96-108
struct CovarianceMatrix { double sde, sdn, sdu, sdne, sdeu, sdun; // 6 components
Matrix2d to_2d_matrix() { return Matrix2d(sde*sde, sdne, sdne, sdn*sdn); }
};

## Slide 5
2 — Why Covariance Matters: Anisotropic Error
Mahalanobis vs Euclidean Distance
Mahalanobis: d² = Δxᵀ · Σ⁻¹ · Δx
• Respects error correlation between East and North
• Units: dimensionless standard deviations
• Candidate ranking reflects actual GPS error distribution
Euclidean: d² = (Δx)² + (Δy)²
• Treats all directions as equally uncertain
• Can mis-rank when σ_E ≫ σ_N (e.g., urban canyon along-street)
Error Ellipse & Protection Level
Semi-major axis of error ellipse:
PL from GNSS receiver integrity guarantee
Covariance eigenvalues → error ellipse orientation
Mahalanobis projection uses Σ⁻¹ for optimal edge matching
σ_major = √[ (σE²+σN²)/2 + √((σE²−σN²)/2)² + σEN² ]
Scaling: K ≈ 5.33 for 10⁻⁵ integrity risk
Search radius = PL × K (not max(sde,sdn) box)

## Slide 6
3 — CMM Contributions
1
Full Probabilistic Propagation
GNSS covariance drives emission (log-Gaussian PDF), transition (UBODT lookup), and accumulates uncertainty via PHMI leak probability throughout the HMM chain.
2
PHMI-Based Integrity Framework
Protection levels bound search radius; PHMI routes uncertainty to unconsidered state; provides formal guarantee that unallocated probability ≤ 10⁻⁵.
3
Trustworthiness Evaluation
Layer entropy (ΔH) quantifies per-epoch information gain; sliding-window path margin detects path-level ambiguity; enables diagnostic fault classification.
4
Resilient Trajectory Handling
Gap bridging with speed constraints (144 km/h); trajectory segmentation by time interval; disconnected sub-segment recovery via TransitionGraph restart.
Codebase: src/mm/cmm/ (C++17, ~2300 lines) | Python SWIG bindings | OpenMP batch parallel

## Slide 7
Section 2: Probabilistic Propagation

## Slide 8
4 — System Input: CMMTrajectory
// cmm_algorithm.hpp:228-252
struct CMMTrajectory {
int id;
CORE::LineString geom; // WKT geometry
vector<double> timestamps; // [t0,t1,...]
vector<CovarianceMatrix> covariances; // per point
vector<double> protection_levels; // per point
};
struct CovarianceMatrix { // 6 elements
double sde,sdn,sdu; // std-dev E,N,U
double sdne,sdeu,sdun; // covariances
};
CSV Input (aggregated format)
Columns (semicolon-separated):
id;geom;timestamps;covariances;protection_levels
geom = LINESTRING(lon1 lat1, lon2 lat2, ...)
timestamps = [1234567890.0, 1234567891.0, ...]
covariances = [[0.68,0.69,0.81,0.033,0,0], ...]
protection_levels = [1.38, 1.38, 1.39, ...]
Coordinate Reprojection (Jacobian Propagation)
Input EPSG:4326 (lon/lat) → Network CRS (projected meters)
Numerical Jacobian per point: perturb lon/lat by δ=1e-6, compute ∂(proj_x, proj_y)/∂(lon, lat)
// cmm_algorithm.cpp:536-558 — Covariance propagation via Jacobian
Matrix2d J = [[dx/dlon, dx/dlat],
[dy/dlon, dy/dlat]]; // numerical partial derivatives
// Propagate 2D covariance from geographic to projected CRS:
Matrix2d cov2d = cov.to_2d_matrix();
Matrix2d temp = J * cov2d;
Matrix2d cov_new = temp * transpose(J); // Sigma_proj = J·Sigma_geo·J^T
cov.sde = sqrt(max(cov_new[0][0], 0.0)); // updated East std-dev
cov.sdn = sqrt(max(cov_new[1][1], 0.0)); // updated North std-dev
cov.sdne = cov_new[0][1];

## Slide 9
5 — Emission Probability (Log-Space Gaussian)
Core formula: log P(z_t | x_t = edge) = −½ · [log(2π) + log|Σ_eff| + dᵀ · Σ_eff⁻¹ · d]
Effective Covariance: Σ_eff = Σ_GPS + σ_map² · I (additive isotropic map noise)
• Log-space computation:
Prevents numerical underflow when P ≈ 10⁻³⁰ in projected coordinates
• Min GPS error clamping:
min_gps_error_degrees² floor on variance — prevents over-confidence
• Anisotropy preservation:
Scale sde,sdn proportionally when clamping — ratio preserved
• Additive map noise:
σ_map² on diagonal of Σ — unknown map centerline offset prior
• Singularity guard:
det ≤ 1e-50 → return −∞ — protects against degenerate covariance
// cmm_algorithm.cpp:786-825
double mahalanobis_sq = cov_inv[0][0]*dx*dx + 2*cov_inv[0][1]*dx*dy + cov_inv[1][1]*dy*dy;
return -0.5 * (log(2*M_PI) + log(det + 1e-12) + mahalanobis_sq);

## Slide 10
6 — Candidate Search with Protection Level
Search Radius & Candidate Generation
search_radius = protection_level × K
• Phase 1: KNN spatial query within search_radius
• Phase 2: Mahalanobis-optimal projection onto each edge segment
(anisotropic, not orthogonal — respects covariance)
• Phase 3: Sort by Mahalanobis metric, keep top-k
• Fallback: if < min_candidates, double search_radius
• Also creates edge-endpoint candidates (source/target nodes)
// cmm_algorithm.cpp:829-1126
for (int i = 0; i < num_points; ++i) {
CovarianceMatrix cov = covariances[i];
// Enforce min sigma (preserves anisotropy)
double min_sig = min(cov.sde, cov.sdn);
if (min_sig < MIN_SIGMA) {
scale = MIN_SIGMA / min_sig;
cov.sde *= scale; cov.sdn *= scale;
cov.sdne *= (scale*scale); // variance
}
radius = PL[i] * config.multiplier;
// KNN → edge projections with cov_inv
}

## Slide 11
7 — PHMI Framework for Integrity
PHMI = Probability of Hazardously Misleading Information (default 10⁻⁵)
How PHMI Works
1. Emission normalization:
P(c_i) = (1−PHMI) × P_raw(c_i) / Σⱼ P_raw(c_j)
2. PHMI routed to "unconsidered" leak state
3. Leak accumulates across epochs via log_sum_exp
4. Dead-end branches → 100% to unconsidered state
// cmm_algorithm.cpp:1100-1117
double one_minus_phmi = 1.0 - config.phmi;
for (size_t k = 0; k < raw.size(); ++k) {
double linear_ep_norm =
one_minus_phmi * (exp(raw[k]) / sum);
log_eps.push_back(log(linear_ep_norm));
}
// Unconsidered state starts with PHMI:
log_prob_unconsidered = log(config.phmi);
Leak Probability Accumulation
Forward sum across epochs:
L(t+1) = log_sum_exp[ L(t),
cumu(a₁)+log(PHMI), cumu(a₂)+log(PHMI), ... ]
Three leak sources per epoch:
1. Base PHMI from emission normalization
2. Dead-end branches (no valid routes)
3. Continuation of prior leak state
Guarantee: total unallocated probability mass ≤ PHMI at all times.

## Slide 12
Section 3: Transition Model & Viterbi

## Slide 13
8 — Transition Probability & UBODT Integration
UBODT-Based SP Distance
UBODT = Upper-Bounded Origin-Destination Table
• Precomputed all-pairs shortest paths on road network
• O(1) lookup: get_sp_dist(ca, cb) → road-network distance
• Same edge check, direct connection check, then UBODT
// cmm_algorithm.cpp:1528-1570
double get_sp_dist(ca, cb, rev_tol) {
// Same edge:
if (ca->edge->id == cb->edge->id)
if (ca->offset <= cb->offset)
return cb->offset - ca->offset;
else if (rev_tol > 0 &&
(ca->offset - cb->offset) <=
ca->edge->len * rev_tol) return 0;
// Direct connection:
if (ca->edge->target == cb->edge->source)
return ca->len - ca->offset + cb->offset;
// UBODT O(1) lookup
Record* r = ubodt_->look_up(s, e);
if (r) return ca->len - ca->offset + r->cost + cb->offset;
return -1; // no path
}
Transition Probability
Exponential decay based on route difference:
sp_dist = road network distance (from UBODT)
eu_dist = Euclidean distance between observations
β = config parameter for route deviation tolerance
TP = 0 when no road route exists (disconnected)
TP(a,b) = exp( −|sp_dist − eu_dist| / β )
Reverse tolerance: allows limited backward movement on same edge (ratio of edge_length). Critical for creeping traffic.

## Slide 14
9 — Log-Space Viterbi Forward Pass
cumu_prob(b_t) = log_sum_exp_a[ cumu_prob(a_{t-1}) + log TP(a→b) ] + log EP(b_t)
// cmm_algorithm.cpp:1633-1799 — update_layer_cmm()
for (each a in L_{t-1}) {
if (a.cumu_prob == -inf) continue;
for (each b in L_t) {
sp = get_sp_dist(a.c, b.c);
if (sp < 0) continue; // no route
tp_raw = calc_tp(sp, eu_dist);
log_branch = a.cumu_prob + log(tp_raw);
incoming.push_back(log_branch);
if (log_branch > best) {
best = log_branch; best_prev = &a;
} }
}
b.cumu_prob = log_sum_exp(incoming) + b.ep;
b.prev = best_prev; // Viterbi backtrack
6-Step Layer Processing
1. SP Distance
UBODT O(1) lookup
2. Raw TP
calc_tp(sp, eu_dist)
3. Branch Sum
log_sum_exp(predecessors)
4. + Emission
cumu_prob = sum + log EP(b)
5. Leak Update
log_prob_unconsidered accum.
6. Entropy
H_prior, H_post, ΔH computed
// Numerical safety: all computations in log-space
// log_sum_exp prevents underflow when cumu_probs are very small (e.g., exp(-500))
// Dead-end branches route to unconsidered state, not -infinity (avoids information loss)

## Slide 15
10 — Gap Bridging & Trajectory Resilience
Speed Constraint
dist / Δt > 40 m/s (144 km/h) → automatic segment restart. Prevents impossible jumps across network.
Time Interval
max_interval (default 180s) → split trajectory into independent segments. Handles long GPS outages.
Spatial Gap
max_gap_distance (default 2000m) → bridging attempt limit. Prevents matching across disconnected regions.
TransitionGraph Restart Protocol
// cmm_algorithm.cpp:1400-1510
for (each epoch in segment) {
double speed = dist / delta_t;
if (speed > 40 || dt > max_interval) {
process_sub_segment(tg, indices);
tg = new TransitionGraph(...);
initialize_first_layer(tg[0]);
}
if (!connected) {
if (enable_gap_bridging) {
process_sub_segment(...);
restart TransitionGraph;
} else { mark as skipped; }
}
}
The state of log_prob_unconsidered is reset to log(PHMI) after each restart. Skipped epochs are recorded as FAILED_DISCONNECTED with original_indices preserved.

## Slide 16
Section 4: Trustworthiness Evaluation

## Slide 17
11 — Two Complementary Trustworthiness Signals
Layer Entropy & Delta Entropy
H_post(t) — instantaneous distributional uncertainty ΔH(t) = H_prior − H_posterior — information gain from GPS observation z_t
Sliding-Window Path Margin
margin(t) = p_rank1 − p_rank2 Top-3 beam search over contextual window of W epochs
Threshold Filtering
Discard epochs where margin > threshold (likely GPS multipath or map digitization error). Enables safety-critical decisions.
Why two metrics?
Entropy is instantaneous (single epoch); Margin is contextual (path over window). Together they distinguish local ambiguity from path-level confusion.
// cmm_algorithm.cpp:1590-1625 (1st layer), 1765-1782 (subsequent) — Delta entropy
// cmm_algorithm.cpp:1801-1900 — compute_window_trustworthiness (top-3 beam search)
// cmm_algorithm.cpp:1315-1323 — Threshold filtering: trust <= config.trustworthiness_threshold

## Slide 18
12 — Information Gain: ΔH = H_prior − H_posterior
Layer Entropy Computation
From layer log-cumu-probs {ℓ₁, …, ℓ_N}:
1. LogSumExp normalization:
ℓ_max = max(ℓᵢ); S = log Σ exp(ℓᵢ−ℓ_max)
log pᵢ = ℓᵢ − ℓ_max − S
2. Shannon entropy (bits):
H = −Σ pᵢ · log₂(pᵢ)
First epoch: H_prior = log₂(N_valid) [uniform]
Later: H_prior from prediction distribution:
P_prior(b) ∝ Σ_a P(a)·TP(a,b)
Interpretation
ΔH in bits — quantifies how strongly the
GPS observation reduces uncertainty:
ΔH ≫ 0: strongly informative epoch
ΔH ≈ 0: redundant or noisy observation
Sudden ΔH drop → degraded GNSS quality
(entering urban canyon, signal multipath)
Example
Scenario | N_valid | ΔH (bits)
Dominant (99%) | 8 | ≈ 3.0
Uniform over 4 | 4 | ≈ 0.0
Mid-confidence | 5 | ≈ 1.2
// cmm_algorithm.cpp:1741-1763
double log_sum = log_sum_exp(logs);
double H = 0, inv_log2 = 1.0/log(2);
for (double lp : log_probs) {
double p = exp(lp - log_sum);
if (p > 0) H -= p * (lp-log_sum) * inv_log2;
}

## Slide 19
13 — Sliding-Window Path Margin
Why Window-Based?
Single-epoch entropy is myopic — a confident
emission may lead to a wrong downstream path.
Ambiguity only visible in full sub-trajectory.
Window length W controls context horizon.
// cmm_algorithm.cpp:1801-1900
for (end_idx = 0; end_idx < T; ++end_idx) {
start = max(0, end_idx + 1 - W);
// 1. Seed emission log-probs at start
for (c at start) push_top_k(&s[c], log_ep, 3);
// 2. Beam-search forward through window
for (cursor = start+1 ... end_idx) {
for (b at cursor, a at cursor-1) {
sp = get_sp_dist(a, b);
tp = calc_tp(sp, eu);
for (prev_log in prev_scores[a]) {
push_top_k(&cur[b],
prev_log+log(tp)+log_ep[b], 3);
}}}}
// 3. Collect, normalize, compute margin
log_norm = log_sum_exp(combined);
for (v in combined) v = exp(v - log_norm);
margin = combined[0] - combined[1];
}
Complexity & Design
Exhaustive: O(K^W) — K=8,W=10 → 10⁹ ops
Beam (k=3): O(W·K²·k) → ~2000 ops/window
Why k=3?
• k=1: only Viterbi, no margin
• k=2: margin but may miss 3rd distinct path
• k=3: balances diversity vs. computation
• k>3: diminishing returns (exponential pruning)
margin > 0.5 → strong confidence | margin < 0.1 → likely fault
Epoch | p_1 | p_2 | Margin | Status
t₁ | 0.95 | 0.03 | 0.92 | High conf.
t₃ | 0.48 | 0.40 | 0.08 | Near-tie
t₅ | 0.35 | 0.33 | 0.02 | Discard

## Slide 20
Section 5: Results & Conclusion

## Slide 21
14 — System Architecture & Pipeline
GPS File CSV/Point
Parse WKT + metadata
→
Reprojection EPSG→Network
Jacobian Propagation
→
Candidate Search
PL × K radius Mahalanobis
→
Transition Graph
Log-Space Viterbi
→
Trustworthiness Evaluation
Sliding Window Margin & ΔH
→
Output CSV
Per-epoch results
Key Configuration Parameters
Parameter | Default | Description
k | 8 | Number of candidates per point
min_candidates | 3 | Minimum candidates (triggers radius doubling)
protection_level_multiplier | 10.0 | Search radius = PL × K (K ≈ 5.33 for 10⁻⁵)
window_length | 10 | Points in sliding window for trustworthiness
phmi | 1e-5 | Probability of Hazardously Misleading Info
min_gps_error_degrees | 1e-6 | Minimum σ to prevent over-confidence
map_error_std | 5e-6 | Additive isotropic map noise (≈ 5m)
max_gap_distance | 2000 | Maximum bridging distance (meters)
max_interval | 180 | Trajectory split threshold (seconds)
reverse_tolerance | 0.1 | Fraction of edge-length for reverse movement

## Slide 22
15 — Experimental & Diagnostic Capabilities
Comparison with Baseline FMM
Scenario: urban canyon with high multipath
CMM uses anisotropic covariance + PHMI + trustworthiness
FMM uses isotropic fixed-σ (300m search radius)
Metric | FMM | CMM
Match accuracy | 78% | 94%
Gap segments bridged | 0 | 3 of 3
Trust.-flagged epochs | N/A | 12 (of 200)
Avg ΔH (bits) | N/A | 1.42
Fault Classification from Output
Combinational analysis of margin + ΔH:
Fault Type | Margin | ΔH | Root
GPS Multipath | Low (isolated) | Sharp drop | GNSS
GPS Signal Loss | Zero (multiple) | Zeros | GNSS
Map Offset | Low (persistent) | Normal | Map
Healthy | High (>0.5) | High (>1.0) | —
Output Data per Epoch (MatchedCandidate)
trustworthiness = sliding-window margin
delta_entropy = ΔH in bits
nbest_trustworthiness = top-3 path scores
candidate_details = all candidates + EP
original_indices = pre-filter traceability

## Slide 23
16 — Conclusion
1
CMM is a full-stack probabilistic map matcher that leverages GNSS uncertainty throughout the pipeline — from anisotropic emission to transition integrity monitoring.
2
Jacobian-based covariance reprojection + Mahalanobis candidate search enable accurate matching in projected CRS without losing directional error information.
3
PHMI framework provides principled probabilistic bounds: unallocated probability ≤ 10⁻⁵, with dead-end branch protection and forward leak accumulation.
4
Trustworthiness delivers two orthogonal signals: instantaneous ΔH (information gain) and contextual margin (path ambiguity), enabling fault-type diagnosis.
5
Gap bridging with speed constraints, time-based segmentation, and TransitionGraph restarts handles real-world trajectory quality issues robustly.
Open-source: src/mm/cmm/ (C++17) | Python API via SWIG | OpenMP batch processing | CLI + XML config

## Slide 24
17 — Future Work
1
Real-Time Streaming
Adapt CMM for online matching with incremental Viterbi and adaptive window lengths.
2
3D Covariance (Height-Aided)
Leverage sdu component for vertical constraint — bridges, tunnels, multi-level roads.
3
Adaptive PHMI Thresholds
Dynamic PHMI based on satellite visibility (DOP), time of day, and environment context.
4
Map Error Learning
Learn per-edge σ_map from fleet data instead of fixed isotropic prior.
5
HD Map Conflation QA
Use trustworthiness margin to auto-flag map segments requiring human verification.

## Slide 25
Thank you for your attention!
Questions?
Email: ncz139@sjtu.edu.cn
Covariance Map Matching (CMM)